## Slide 1: 登机与离机策略的最优化讨论 The Optimal Boarding & Disembarking Method
IMMC 22768821
上海市实验学校 Shanghai Experimental School

## Slide 2: 模型分析结构 Model Analysis & Structure
图 本模型的结构
Fig. The structure of our model
图 登机流程图
Fig. Flow chart of boarding

## Slide 3: 假设 Assumptions
过道的宽度恰好能容纳一名乘客。
The total width of a passenger and his luggage is similar to the width between rows.
  这可以把连续模型变为离散的并简化计算。
  This can turn the continuous model into a discrete model to simplify the calculation.
行李架足够大，能容纳任意大小的行李。
The luggage racks are designed to be adequate for any reasonable amount of luggage.
  把行李放在行李架上和把行李挤到座位里在时间上相等
  Passengers spend the same time putting luggage into the rack as putting the luggage into the seat
在一个特定单元格中，乘客速度是一个常量。
In a particular cell, is a fixed value.
  维护了模型的离散性。
  Ensures the discreteness of the model.
  只在计算距离时有用
  Only appeared in the calculation of total distance
  在同一个单元格中，速度变化不大，并且平均速度与我们所用的平均值大约相等。
  The velocity wouldn’t change much in a particular cell, and the actual average speed is approximately equal to the average we’ve made

## Slide 4: 假设的解释 Justification for the Assumption
关于最后一条假设的解释
The explanation for the last assumption made in the previous slide
The more continuous : the passengers’ speed at every time step
The more discrete : the passengers’ speed at every time step
Every can be seen as a distinct point on .
Therefore, the summation (or integral) of these two defined velocities will roughly amount to the same value.

## Slide 5: 变量表 Notations
Constant A: won’t change in the whole scope. (Nature of Model)
Constant B: may change in the whole scope, but won’t change for a fixed set of passengers and a set plane. (Nature of Aircraft and Method)
Variable: varies for different initial sequences of passengers. (Nature of Passengers)
常量A：在整个过程中不会变化。（模型的性质）
常量B：在整个过程中会变化，但对于一个乘客群体不会变化。（飞机与方法的性质）
变量：随着时间变化而改变。（乘客的性质）
*以下演讲中的变量若初次出现会伴随详细解释。
*In the following presentation, variables that emerge for the first time will be accompanied by detailed explanations.
Notes: 如ppt所言

## Slide 6: 定义 Definitions
时间 Time
  定义“时间”为无量纲。
  Define “time” as partitions of , without units.
  不会改变相对的最优策略，可以简化模型。
  Wouldn’t change the relatively best strategy and could simplify the model.
速度 Velocity
  定义“速度” 为通过一个单元格长度 所需的时间。
  In the model, we define the “velocity” as the time spent to move the length of a cell .

## Slide 7: 模型总览 Overview of Our Model
图 模型总览
Fig. Overview of our model

## Slide 8: 构建数学模型计算登机时间（常规状态） Devising a Model to Calculate Total Boarding Time (Under Regular States)
坐标系的构建 - The construction of the coordinate
图 坐标系的构建
Fig. The construction of the coordinate
对于没人坐或是不对齐的座位，我们将其按照实际位置补入坐标空间中。
For unoccupied or unaligned seats, we add them into the coordinate according to their actual position.
每一个位置都存在唯一的单元格与之对应。
only one correspondent cell exists in each position.
比如该墙体仍然被当作坐标格处理
For example, this wall is still taken as several cells.
Cell 1
Cell 2

## Slide 9: 构建数学模型计算登机时间（常规状态） Devising a Model to Calculate Total Boarding Time (Under Regular States)
需要注意的地方 – Places to take notice
  我们这里形式地定义了拥堵状态下的这样的定义会对事后的计算造成不便
  Here, we define for the integrity of our definitions, but this may cause inconvenience for later calculations.
  事实上我们将在后面定义“拥堵程序”来解决这一问题
  In fact, we’ll define the congestion state later to tackle this issue.
  但在下面得到正常状态下的递推式的过程中，我们将默认提到的乘客均处于行走状态
  But in the following process of deriving the recursion formula in the normal state, we’ll tacitly assume that all passengers are in the walking state.

## Slide 10: 构建数学模型计算登机时间（常规状态） Devising a Model to Calculate Total Boarding Time (Under Regular States)
根据人流密度计算乘客的速度 - Calculating passengers’ speed with the crowd density
  在本模型中定义的人流密度 – The crowd density defined in our model
  选择4作为可见度范围的原因 – The reason for taking 4 as the visibility range
    4格的距离较为适中（3.2m）较为符合现实
    4 cells combined have a moderate range of 4.2 metres, which is also quite realistic.
    在我们的模型中，可见度范围同时决定了我们算法中的时间间隔的长短，因此选择4之后我们可以选取模拟间隔为或不必为更小的间隔（）
    In our model, the visibility range simultaneously affects the interval in our algorithm. Therefore, choosing 4 as the visibility range can avoid unnecessary complexity.

## Slide 11: 构建数学模型计算登机时间（常规状态） Devising a Model to Calculate Total Boarding Time (Under Regular States)
根据人流密度计算乘客的速度 - Calculating passengers’ speed with the crowd density
  格林希尔茨（Greenshields）速度-人流密度线性关系模型（论文中引用3）
  Greenshields speed-density linear model (Ref. 3 in the essay)

## Slide 12: 构建数学模型计算登机时间（常规状态） Devising a Model to Calculate Total Boarding Time (Under Regular States)
根据乘客分布计算人流密度 – Calculating crowd density under a given passenger distribution
  由两个分别代表乘客“能见度”与过道中乘客状态分布的向量数乘得到
  Calculated through the dot product of two vectors representing the passenger’s visibility and the overall distribution in the aisle. (or the existence factor)
图 两个向量的直观表示
Fig. The intuitive illustration of the visibility and existence vectors

## Slide 13: 构建数学模型计算登机时间（常规状态） Devising a Model to Calculate Total Boarding Time (Under Regular States)
根据速度推出乘客分布 - Calculating passenger distribution with speed
  等价于通过速度计算（乘客在时刻的单元格编号）
  equivalent to calculating (the index of passenger ’s current cell at time ) with the speed of all passengers.
  对于某一个乘客，由于我们之前的假设——一位乘客在一格单元格内的速度是恒定不变的——我们只需比对他走到哪两个单元格的时间包含了时刻。
  For a specific passenger, due to our previous assumption (a passenger’s speed remains constant within a singular cell), we only need to calculate the time a passenger needs to enter every cell and find out which total time of the two adjacent cells include .
  我们使用部分和跟踪并得出结果 – We use partial summation to get the formulas.

## Slide 14: 构建数学模型计算登机时间（常规状态） Devising a Model to Calculate Total Boarding Time (Under Regular States)
总结——我们得到的递推式 – The overall recursion formula we get
  我们的模型一直到“更新速度”这一层都是线性的，而根据真实速度与模型中速度的反比关系，我们将会得到一个线性模型。（这一部分将会在之后的敏感度分析中得到验证）
  Our model is linear until the final stage (or the first slide presented in this part), so according to the inverse proportional relationship between real-life velocity and the velocity in our model, we’ll get a linear model. (this quality will be verified later in the Sensitivity Analysis part)
  因此，我们可以得到下述由前一时刻所有乘客的速度状态组的线性组合得到的线性递推公式。
  Therefore, we can get the linear recursion formula with the whole state of passenger velocities as the previous time step, as shown below.

## Slide 15: 构建数学模型计算登机时间（拥挤状态） Devising a Model to Calculate Total Boarding Time (Under the Crowded States)
解决遗留问题——拥挤状态的情形 – Tackling the remaining problems: the congestion state
状态的分析 – Analysis of different states
摆放行李 – Stowing luggage
  总时间
    表示标准状况下乘客放行李的时间 - represents the standard luggage stowing time of a passenger
    是乘客的“不守规则指数” - is the discompliance index of a passenger
    越大，这位乘客需要更多时间放行李 – The higher is, the longer stowing time a passenger needs
就座与让座 - Getting seated and offering seats
  乘客的让座时间正比于其座位距离过道的单元格数
  The time that a passenger needs to offer his seat is proportional to the number of cells separating his seat and the aisle
  取该行中最长时间为标准
  We take the longest time to offer a seat among the row

## Slide 16: 构建数学模型计算登机时间（拥挤状态） Devising a Model to Calculate Total Boarding Time (Under the Crowded States)
解决遗留问题——拥挤状态的情形 – Tackling the remaining problems: the congestion state
状态的分析 – Analysis of different states
就座与让座 - Getting seated and offering seats
  让座时间便可以直接通过初始队列的顺序计算。The time to offer seats can be calculated once given the original queue.
    原因：队伍对同行乘客的保序性 Reason – the preservation of sequence in the queue.
图 让座程序
Fig. Offering a seat

## Slide 17: 构建数学模型计算登机时间（拥挤状态） Devising a Model to Calculate Total Boarding Time (Under the Crowded States)
解决遗留问题——拥挤状态的情形 – Tackling the remaining problems: the congestion state
状态的转换 – The interconversion of states
状态参量 – The state parameters
  我们使用表示乘客的状态，且我们定义： – We use to determine passenger’s state, and we define:
  这样，
转换公式 – The interconversion formula
  递归地计算 recursive calculations
  （为方便起见）下标大或小直接表示顺序后或前 subscript’s magnitude reflect the sequence in the queue

## Slide 18: 构建数学模型计算登机时间（拥挤状态） Devising a Model to Calculate Total Boarding Time (Under the Crowded States)
解决遗留问题——拥挤状态的情形 – Tackling the remaining problems: the congestion state
状态的转换 – The interconversion of states
转换公式 – The interconversion formula
  我们使用了如下方式更新状态，达到效果 – We used the following method to update the states.
  最终转换的效果如下。Below is shown the mechanism, which fits our flow chart as shown in the beginning.
  不难发现，最终的关系仍然保持线性。It’s clear that the relationship remains linear.

## Slide 19: 构建数学模型计算登机时间（拥挤状态） Devising a Model to Calculate Total Boarding Time (Under the Crowded States)
解决遗留问题——拥挤状态的情形 – Tackling the remaining problems: the congestion state
状态的转换 – The interconversion of states
剔除公式 – Deleting from the queue
  当乘客到达座位，我们通过将其剔除队列来更新以继续进行运算，不会影响到前述算法。
  When a passenger reaches his seat, we delete him from the queue to update and continue with the calculations without affecting the previous algorithm.

## Slide 20: 构建数学模型计算登机时间（总时间） Devising a Model to Calculate Total Boarding Time (Total time)
计算总时间 – Calculating total time
  将刚才的合并起来即可获得总时间 – Combine the previously discussed factors, and we get the total time
  引入几个概念 – Introducing several new concepts
    为乘客从停下放行李到就座的时间 - is the time passenger spends from stowing luggage to getting seated.
    乘客不需要排队的次数 - stands for the times that passengers do not need to line in a queue
    为乘客在第个单元格中花费的时间 - is the time passenger spends in the cell.

## Slide 21: 构建数学模型计算登机时间（总时间） Devising a Model to Calculate Total Boarding Time (Total time)
计算总时间 – Calculating total time
  则我们可以得到总时间 – Then, we can calculate the total time spent by .
  那么整个登机过程的时间为 – And the total time of boarding is:

## Slide 22: 构建数学模型计算登机时间（并行性） Devising a Model to Calculate Total Boarding Time (Parallelity)
并行性 - Parallelity
关于并行性真正意义的探讨 – The discussion into the deep meanings of parallelity
  “并行性”的定义 – The definition of parallelity
    提出背景（定性）- Background (qualitative)
      希望让更多的单元格过道被占用（即有乘客在其中放行李），使得系统的效率得到提升
      We hope that more aisle cells are occupied (meaning that there are passengers stowing luggage in that cell), thereby enhancing boarding efficiency.
    我们对于并行性的定义
      简言之——过道占有率 – Aisle occupation rate in brief
      假设过道中被占有的单元格数量为，总单元格数为，则我们定义：
      Suppose there are cells occupied in total and a total of aisle cells.

## Slide 23: 构建数学模型计算登机时间（并行性） Devising a Model to Calculate Total Boarding Time (Parallelity)
并行性 - Parallelity
关于并行性真正意义的探讨 – The discussion into the deep meanings of parallelity
  “模型基础”（半定量分析）- Model basis (semi-quantitative analysis)
    前述计算表明乘客的速度遵循递推式，并且遵循线性模型的关系
    Previous calculations infer that the velocities of passengers follow a recursion formula and that they follow a linear pattern.
    而想让总时间变小，本模型中定义的“速度”需要尽量小
    Therefore, to minimise total time, the velocity (the one defined in our model) should also be minimised.

## Slide 24: 构建数学模型计算登机时间（并行性） Devising a Model to Calculate Total Boarding Time (Parallelity)
并行性 - Parallelity
关于并行性真正意义的探讨 – The discussion into the deep meanings of parallelity
  “模型基础”（半定量分析）- Model basis (semi-quantitative analysis)
    因此希望让“速度”的增加次数尽可能小，或是尽可能长时间维持在最小值
    That’s why we want the velocity to increase fewer times or maintain its minimum for an extended period of time.
    所以希望过道的占用率更大，这样乘客能够保持更长时间（现实中的）的最大速度，直到所有在过道中的人再次开始放行李
    So, by hoping the aisle has higher occupancy, passengers can maintain the maximum speed (in reality) until all the passengers in the aisle start stowing luggage again.
    因此我们使用“过道占有率”来作为总时间的衡量指标
    Therefore, we use aisle occupancy to measure total time.

## Slide 25: 构建数学模型计算登机时间（并行性） Devising a Model to Calculate Total Boarding Time (Parallelity)
并行性 - Parallelity
关于并行性真正意义的探讨 – The discussion into the deep meanings of parallelity
  数学推导（全定量分析）- Mathematical deduction (quantitative analysis)
    结论1（满格的最优性）- Claim 1 (the optimality of all cells being occupied)
    该结论从另一方面也验证了本模型的正确性。
    This claim, on the other hand, also justified our model.
      调整法结合理想状态分析
      the adjustment method & analysis on idealistic circumstances
    结论2将会在之后的多机型部分出现。
    Claim 2 will appear later in the TETA and Flying Wing part.
论文所言的具体数学过程我们将不再赘述。
We’ll not elaborate on the essay-based strict proof.

## Slide 26: 离机与登机的关联 Relationship Between Boarding and Disembarking
对于每名乘客来说，其离机过程就是其登机过程的逆过程。
For each passenger, the disembarking process is the reverse of the boarding process.
让过道尽量被占用，以达到最高的并行性。
The aisles are maximally utilised in terms of parallelity.
不存在让位的可能（因为走廊被堵住），简单的从外到内。
There’s no possibility of offering cells, for the aisle is blocked when passengers are getting the luggage out.
乘客以理想方式排队，并行性高于登机，所需时间会短于登机。
Passengers queue as the ideal way, having higher parallelity than boarding. Therefore, the time needed is shorter than boarding.
图 最优离机方案
Fig. The optimal disembarking strategy

## Slide 27: 满意度指数 Satisfaction Index
衡量乘客的不满意度。
Measures the dissatisfaction of passengers.
  排队时间 Queuing time
  让座时间 Time offering seats
  同一排内乘客登机时间的标准差 The standard variance of the boarding time of the passengers in the same row
    考虑家庭拆散问题 families may be separated
    论文中并未直接指明，特此标注 It was not directly shown in the essay, so we point this out for your reference.
  总不满意度是这三个因素的加权和，三个因素的权值分别是1，250与10
  The total dissatisfaction is the weighted sum of the three factors, the weight respectively 1, 250 and 10.
为什么是1，250，10三个数？
Why 1, 250 and 10?
  1是为了标准化
  1 is for standardisation
  统一量级并考察重要性
  Unite magnitudes & importance
    较为统一的量级可以使最终的总满意指数综合这三项指标，而不是偏重其中某一项
    Once united the magnitudes, the dissatisfaction index can rather equally reflect the three aspects of passengers’ satisfaction.

## Slide 28: 模拟结果 Results of Simulation

## Slide 29: 敏感度分析 Sensitivity Analysis
如何对我们的模型进行敏感度分析？
How to conduct a Sensitivity Analysis on Our Model?
  使用拟合程度进行定量衡量
  Use Compliancy Index to measure in concrete figures
  对改变的可预测性
  Predictability of Changes
  结论与模型证明的变化关系
  Relationship proved by Claims and Our Model

## Slide 30: 敏感度分析 Sensitivity Analysis
情况一：更长的行李放置时间
Case 1: A Longer Stowing Time
  使用的随机分布模型：Sigmoid模型
  Use Sigmoid Model for Random Distribution
    统计学常用模型
    Commonly Used in Statistics
    由函数决定的适用范围：实数指定范围，
    两端接近极值，中间较为线性
    Usage determined by nature of function: A Custom Range,
    reaching the limit at both ends with linear in the middle
图 Sigmoid模型范例
Fig. Sigmoid Model Demonstration

## Slide 31: 敏感度分析 Sensitivity Analysis
情况一：更长的行李放置时间
Case 1: A Longer Stowing Time
  如何区分稳定和不稳定？（总体尺度上）
  How to distinguish between Stable and Unstable? (Overall Timestep)
    稳定：线性图像
    Stable: Linear Graph
    不稳定：无明显规律
    Unstable: No Obvious Relationship
  方差（差异化程度）的图像
  The Graph of Variance
    稳定：先为上凸函数（变化率逐渐递减），后为线性
    Stable: Rate of Changing Decrease followed by Linear
    不稳定：无线性阶段
    Unstable: No Linear State

## Slide 32: 敏感度分析 Sensitivity Analysis
情况一：更长的行李放置时间
Case 1: A Longer Stowing Time
图 放置行李时间影响比较（方差）
Fig. Comparison on Longer Stowing Time, Variance

## Slide 33: 敏感度分析 Sensitivity Analysis
情况一：更长的行李放置时间
Case 1: A Longer Stowing Time
随机登机敏感度较高，由前到后登机敏感度较低
Random boarding is the most sensitive while Front-to-Back method seems totally not sensitive
图 放置行李时间影响比较（总时间）
Fig. Comparison on Longer Stowing Time, Overall Time

## Slide 34: 敏感度分析 Sensitivity Analysis
情况二：插队
Case 2: Queue Jumping
两个方案均为敏感方案，会对结果造成巨大的影响
Both Methods are Sensitive which makes a Big Impact on Total Results
图：插队影响比较
Fig. Comparison on Queue Jumping

## Slide 35: 敏感度分析 Sensitivity Analysis
情况三：乘客数量的减少
Case 3: Reduction of Passengers
随机登机最为敏感（点的分布最远），由后到前登机依然十分稳定
Random Boarding is the most Sensitive (Furthest Distribution of Points), Back-to-Front Method still not so sensitive
图：乘客人数减少影响比较
Fig. Comparison on Reducing Passengers

## Slide 36: 敏感度分析 Sensitivity Analysis
结论
Conclusion
  随机登机相较于由前到后登机远远更为敏感
  Random Boarding is Far More Sensitive than Front-to-Back Method
  原因：随机化的登机顺序的任何非正常行为均会造成不可衡量的影响
  Justification: Randomized Boarding Sequence can result in Immeasurable Effects
  由后到前方案综合表现最佳
  Back-to-Front Method Performs the Best Overall
  原因：由后到前和由前到后均为低敏感度方案，但由后到前的总时间和满意度最高
  Justification: Back-to-Front and Front-to-Back are the least sensitive, but Overall Time and distinguish Back-to-Front from Front-to-Back

## Slide 37: 应用到不同机型（坐标划分） Application to Different Aircrafts (The division of coordinates)
Flying Wing Aircraft
  采用了三维坐标形式
  We adopted three-dimensional coordinates.
  将每一块看作互相独立的部分
  We see every block as independent parts
图 Flying Wing 坐标划分
Division of coordinates in Flying Wing
Main Aisle Cells
Block Aisle Cells

## Slide 38: 应用到不同机型（坐标划分） Application to Different Aircrafts (The division of coordinates)
图 TETA 坐标划分
Division of coordinates in TETA

## Slide 39: 应用到不同机型（准备部分） Application to Different Aircrafts (Preparation)
结论2：“占有率”引导的最优化 Claim 2 – Optimization based on occupational rate
  确定优先级 Determining the priority
    主过道 Main cells
    块过道 Block cells
  引入效率变量 Introducing the efficiency variable
    仅为了做出不同块的定性解释
    We introduce this variable solely for the purpose of qualitative analysis of multiple blocks.

## Slide 40: 应用到不同机型 Application to Different Aircrafts
图 最优登机步骤流程图
Fig. Flow chart for the optimal boarding method
两种区块划分
Two block division schemes

## Slide 41: 应用到不同机型 Application to Different Aircrafts
结论 Conclusion
  局部最优 Regional optimum
    采用前述最快的 Steffen sub-perfect 方案
  （本模型关键）维护最优
  The key of our model – maintaining optimality
    由到登机（从内到外）
    Boarding from to (inner to outer)
    “备用人”
    Backup Passengers
    贪心算法
    Greedy Algorithm
图 理想登机方案
Fig. Ideal Boarding Scheme

## Slide 42: 应用到不同机型 Application to Different Aircrafts
结论 Conclusion

## Slide 43: 优缺点 Strengths & Weaknesses
优点
  准确性
  多样性
  有效性
缺点
  复杂性
  难于操作
Strengths
  Accuracy
  Universality
  Efficiency
Weaknesses
  Complexity
  Difficult to operate

## Slide 44: 给航空公司的建议信 A Letter to Airline Executives
两个主要因素 Two factors:
  人性化 Hominization
  高效 Efficiency
三条有效建议 Three suggestions:
  防止主过道拥堵
  Avoid blocks in general aisles
  为行李提供足够空间
  Provide enough space for luggage
  防止不必要的插队
  Prevent unnecessary queue-jumping