## Slide 1: The Optimal Boarding & Disembarking Method
IMMC 22768821
Shanghai Experimental School

## Slide 2: Table of Contents
The structure of our model
Analysis of the problem
Optimization and Its Applications (Disembarking)
Sensitivity Analysis
Extensions of Our Model
Conclusion & Reflection

## Slide 3: Part 1 The structure of our model
IMMC22768821

## Slide 4: Model Analysis & Structure
Fig. The structure of our model
Fig. Flow chart of boarding

## Slide 5: Critical Assumptions
The luggage racks are designed to be adequate for any reasonable amount of luggage.
  Passengers spend the same time putting luggage into the rack as putting the luggage into the seat
In a particular cell, is a fixed value.
  Ensures the discreteness of the model.
  Only appeared in the calculation of total distance
  The velocity wouldn’t change much in a particular cell, and the actual average speed is approximately equal to the average we’ve made
Notes: 结构化的有限元模拟，比较显然的假设

## Slide 6: Justification for the Assumption
The explanation for the last assumption made in the previous slide
The more continuous : the passengers’ speed at every time step
The more discrete : the passengers’ speed at every time step
Every can be seen as a distinct point on .
Therefore, the summation (or integral) of these two defined velocities will roughly amount to the same value.
Notes: 解释没有必要继续细讲，假设在这个架构下是显然的，口头讲即可

## Slide 7: Definitions
Time
  Define “time” as partitions of , without units.
  Wouldn’t change the relatively best strategy and could simplify the model.
Velocity
  In the model, we define the “velocity” as the time spent to move the length of a cell .
Notes: （1）量纲问题
（2）velocity的定义式形式问题

## Slide 8: Part 2 Analysis of the problem
IMMC22768821

## Slide 9: Overview of math model
Fig. Overview of our model

## Slide 10: Total Boarding Time (Under Regular States)
The construction of the coordinate
Fig. The construction of the coordinate
For unoccupied or unaligned seats, we add them into the coordinate according to their actual position.
only one correspondent cell exists in each position.
For example, this wall is still taken as several cells.
Cell 1
Cell 2

## Slide 11: Total Boarding Time (Under Regular States)
Calculating passengers’ speed with the crowd density
  The crowd density defined in our model
  The reason for taking 4 as the visibility range
    4 cells combined have a moderate range of 4.2 metres, which is also quite realistic.
    In our model, the visibility range simultaneously affects the interval in our algorithm. Therefore, choosing 4 as the visibility range can avoid unnecessary complexity.

## Slide 12: Total Boarding Time (Under Regular States)
Calculating passengers’ speed with the crowd density
  Greenshields speed-density linear model (Ref. 3 in the essay)

## Slide 13: Total Boarding Time (Under Regular States)
Calculating crowd density under a given passenger distribution
  Calculated through the dot product of two vectors representing the passenger’s visibility and the overall distribution in the aisle. (or the existence factor)
Fig. The intuitive illustration of the visibility and existence vectors

## Slide 14: Total Boarding Time (Under Regular States)
Calculating passenger distribution with speed
  equivalent to calculating (the index of passenger ’s current cell at time ) with the speed of all passengers.
  For a specific passenger, due to our previous assumption (a passenger’s speed remains constant within a singular cell), we only need to calculate the time a passenger needs to enter every cell and find out which total time of the two adjacent cells include .
  We use partial summation to get the formulas.

## Slide 15: Total Boarding Time (Under Regular States)
The overall recursion formula we get
  Our model is linear until the final stage (or the first slide presented in this part), so according to the inverse proportional relationship between real-life velocity and the velocity in our model, we’ll get a linear model. (this quality will be verified later in the Sensitivity Analysis part)
  Therefore, we can get the linear recursion formula with the whole state of passenger velocities as the previous time step, as shown below.

## Slide 16: Total Boarding Time (Under Crowded States)
Tackling the remaining problems: the congestion state
Analysis of different states
Stowing luggage
    represents the standard luggage stowing time of a passenger
    is the discompliance index of a passenger
    The higher is, the longer stowing time a passenger needs
Getting seated and offering seats
  The time that a passenger needs to offer his seat is proportional to the number of cells separating his seat and the aisle
  We take the longest time to offer a seat among the row

## Slide 17: Total Boarding Time (Under Crowded States)
Tackling the remaining problems: the congestion state
Analysis of different states
Getting seated and offering seats
  The time to offer seats can be calculated once given the original queue.
    Reason – the preservation of sequence in the queue.
Fig. Offering a seat

## Slide 18: Total Boarding Time (Under Crowded States)
Tackling the remaining problems: the congestion state
The interconversion of states
The state parameters
  We use to determine passenger’s state, and we define:
  Therefore, .
The interconversion formula
  recursive calculations
  subscript’s magnitude reflect the sequence in the queue

## Slide 19: Total Boarding Time (Under Crowded States)
Tackling the remaining problems: the congestion state
The interconversion of states
The interconversion formula
  We used the following method to update the states.
  Below is shown the mechanism, which fits our flow chart as shown in the beginning.
  It’s clear that the relationship remains linear.

## Slide 20: Total Boarding Time (Under Crowded States)
Tackling the remaining problems: the congestion state
The interconversion of states
Deleting from the queue
  When a passenger reaches his seat, we delete him from the queue to update and continue with the calculations without affecting the previous algorithm.

## Slide 21: Total Boarding Time (Total time)
Calculating total time
  Combine the previously discussed factors, and we get the total time
  Introducing several new concepts
    is the time passenger spends from stowing luggage to getting seated.
    stands for the times that passengers do not need to line in a queue
    is the time passenger spends in the cell.

## Slide 22: Total Boarding Time (Total time)
Calculating total time
  Then, we can calculate the total time spent by .
  And the total time of boarding is:

## Slide 23: Part 3 Optimization and Its Applications (Disembarking)
IMMC22768821

## Slide 24: Vertical Optimization (Parallelity)
Parallelity
The discussion into the deep meanings of parallelity
  The definition of parallelity
    Background (qualitative)
      We hope that more aisle cells are occupied (meaning that there are passengers stowing luggage in that cell), thereby enhancing boarding efficiency.
    Our definition on Parallelity
      Aisle occupation rate in brief
      Suppose there are cells occupied in total and a total of aisle cells.

## Slide 25: Vertical Optimization (Parallelity)
Parallelity
The discussion into the deep meanings of parallelity
  Model basis (semi-quantitative analysis)

## Slide 26: Vertical Optimization (Parallelity)
Parallelity
The discussion into the deep meanings of parallelity
  Mathematical deduction (quantitative analysis)
    Claim 1 (the optimality of all cells being occupied)
    This claim, on the other hand, also justified our model.
      the adjustment method & analysis on idealistic circumstances
    Claim 2 will appear later in the TETA and Flying Wing part.
We’ll not elaborate on the essay-based strict proof.

## Slide 27: Modelling & Optimization of Disembarking
The starting point and destination of the passengers are exchanged.
The aisles are maximally utilised in terms of parallelity.
There’s no possibility of offering cells, for the aisle is blocked when passengers are getting the luggage out.
Passengers queue as the ideal way, having higher parallelity than boarding. Therefore, the time needed is shorter than boarding.
Fig. The optimal disembarking strategy

## Slide 28: Horizontal Optimization (Satisfactory Index)
Measures the dissatisfaction of passengers.
  Queuing time
  Time offering seats
  The standard variance of the boarding time of the passengers in the same row
  The total dissatisfaction is the weighted sum of the three factors, the weight respectively 1, 250 and 10.

## Slide 29: 模拟结果 Results of Simulation

## Slide 30: 模拟结果 Results of Simulation
Shortest time: Steffen Sub-Perfect
Highest Satisfactory: Back to Front

## Slide 31: Part 4 Sensitivity Analysis
IMMC22768821

## Slide 32: Sensitivity Analysis
Case 1: A Longer Stowing Time
  Random boarding is the most sensitive while Front-to-Back method seems totally not sensitive
Case 2: Queue Jumping
  Both Methods are Sensitive which makes a Big Impact on Total Results
Case 3: Reduction of Passengers
  Random Boarding is the most Sensitive (Furthest Distribution of Points), Back-to-Front Method still not so sensitive

## Slide 33: Sensitivity Analysis
Conclusion
  Random Boarding is Far More Sensitive than Front-to-Back Method
  Justification: Randomized Boarding Sequence can result in Immeasurable Effects
  Back-to-Front Method Performs the Best Overall
  Justification: Back-to-Front and Front-to-Back are the least sensitive, but Overall Time and distinguish Back-to-Front from Front-to-Back

## Slide 34: Part 5 Extensions of Our Model
IMMC22768821

## Slide 35: Application to Different Aircrafts (Coordinates)
Flying Wing Aircraft
  We adopted three-dimensional coordinates.
  We see every block as independent parts
Fig. Division of coordinates in Flying Wing
Main Aisle Cells
Block Aisle Cells

## Slide 36: Application to Different Aircrafts (Coordinates)
Fig. Division of coordinates in TETA

## Slide 37: Application to Different Aircrafts (Optimisation)
Claim 2 – Optimization based on occupational rate
  Determining the priority
    Main cells
    Block cells
  Introducing the efficiency variable
    We introduce this variable solely for the purpose of qualitative analysis of multiple blocks.

## Slide 38: Application to Different Aircrafts (Optimisation)
Fig. Flow chart for the optimal boarding method
Two block division schemes

## Slide 39: Application to Different Aircrafts (Conclusions)
Conclusion
  Regional optimum
    Steffen sub-perfect
  The key of our model – maintaining optimality
    Boarding from to (inner to outer)
    Backup Passengers
    Greedy Algorithm
Fig. Ideal Boarding Scheme

## Slide 40: Application to Different Aircrafts (Conclusions)
Conclusion

## Slide 41: Part 6 Conclusion & Reflection
IMMC22768821

## Slide 42: Strengths & Weaknesses
Strengths
  Accuracy
  Universality
  Efficiency
Weaknesses
  Complexity
  Difficult to operate

## Slide 43: Thanks